Computer Organization Lab 1
0113110 Po-han Chen, 0316213 Yu-wen Pwu
Architecture Diagram
We’ve implemented the ALU accordingly. (ie. We haven’t changed the architectures specified in the HW document.)
alu_single (1 bit)	alu (32 bit)

For the final result, please refer to the appendix at the end of the report.
Detailed Description of the Implementation
We have designed a 32-bit ALU that supports common arithmetic operations including: And, Or, Add, Subtraction, Nor, Nand and Comparisons (Set less than, Set greater than, Set less or equal, Set greater or equal, Set equal, Set not equal).
The design is composed of 32 1-bit ALUs interconnected sequentially. Let’s denote the ALU for the LSB (least significant bit) by ALU0, the ALU for the second LSB by ALU1 and all the way to the ALU for the MSB (most significant bit) by ALU31.
- For ALUi, where 1 ≤ i ≤ 31:
  - (Input) src1 and src2, the 2 single-bit input numbers, are connected to src1[i] and src2[i] respectively.
  - (Input) less, the input for the comparison signals, is connected to 0 (constant).
  - (Input) src1_invert and src2_invert, indicating whether the input bit should be flipped, are connected to src1_invert and src2_invert respectively.
  - (Input) cin, the carry-in for this ALUi, is connected to cin[i].
  - (Input) operation, indicating the type of arithmetic operation to be carried out, is connected to operation.
  - (Output) result is the calculated result of ALUi.
  - (Output) cout, the carry-out for bit i, connects with the carry-in for the next bit (ie. cin[i + 1]).
- For ALU0, everything is the same except that:
  - (Input) less, the input for the comparison signals, is connected to less.
- Regarding the connections outside the 1-bit ALUs, we considered them reversely during implementation:
  - cin[0], the carry-in for the LSB, is:
    1, if ALU_control is 4’b0110 (Subtract) or 4’b0111 (Compare)
    0, otherwise.
  - src1_invert, indicating whether src1 should be inverted, is:
    1, if ALU_control is 4’b1100 (Nor) or 4’b1101 (Nand)
    0, otherwise.
  - src2_invert, indicating whether src2 should be inverted, is:
    1, if ALU_control is 4’b1100 (Nor), 4’b1101 (Nand), 4’b0110 (Subtract) or 4’b0111 (Compare)
    0, otherwise.
  - operation is:
    2’b00, if ALU_control is 4’b0000 (And) or 4’b1100 (Nor)
    2’b01, if ALU_control is 4’b0001 (Or) or 4’b1101 (Nand)
    2’b10, if ALU_control is 4’b0010 (Add) or 4’b0110 (Subtract)
    2’b11, otherwise.

Problems Encountered and Solutions

Lesson Learned (If Any)
1. 肝毋好，人生係黑白的；
   肝若好，作業係空白的。
2. Verilog 2001 added the generate block, which is very handy to instantiate an abundance of modules.
3. Xilinx Vivado Design Suite is much more powerful than its legacy EDA tool – Xilinx ISE Design Suite.