Computer Organization Lab 2
0113110 Po-Han Chen, 0316213 Yu-Wen Pwu
Architecture Diagram

Detailed Description of the Implementation
ALU Operations (input [3:0] ALU_op_i)
Case (ALU_op_i)
  - 0: src1_i & src2_i
  - 1: src1_i | src2_i
  - 2: src1_i + src2_i
  - 6: src1_i - src2_i
  - 7: src1_i < src2_i
  - 12: ~(src1_i | src2_i)
  - 14: src2_i_signed >>> src1_i_signed
  - 15: src2_i << 16
- ALU Control (input [5:0] funct_i)
  Case (funct_i)
  - 3: ALUCtrl_o = 14; // SRA
  - 7: ALUCtrl_o = 14; // SRAV
  - 32: ALUCtrl_o = 2; // ADD
  - 34: ALUCtrl_o = 6; // SUB
  - 36: ALUCtrl_o = 0; // AND
  - 37: ALUCtrl_o = 1; // OR
  - 42: ALUCtrl_o = 7; // SLT
- Decoder Output Signals (input [4:0] instr_op_i;)
  - RegWrite = 1, if instr_op_i ∈ {0, 35, 8, 9, 15, 13}
    R-type, Load, ADDI, SLTIU, LUI, ORI
    -> Need to write result to some register
  - ALU_op =
          (instr_op_i == 35 || instr_op_i == 43) ? 2 : // Load or Store -> add
          (instr_op_i == 4 ? 6 : // Branch -> sub
          (instr_op_i == 8 ? 2 : // ADDI -> add
          (instr_op_i == 9 ? 7 : // SLTIU -> lt
          (instr_op_i == 13 ? 1 : // ORI -> or
          (instr_op_i == 15 ? 15: // LUI -> Left shift immediate by 16
          4'b1111))))); // Else -> check with funct in instruction
  - ALUSrc = 1, if instr_op_i ∈ {35, 43, 8, 9, 15, 13}
    Load, Store, ADDI, SLTIU, LUI, ORI
    -> Multiplexer selects [15:0] as the second ALU source
  - RegDst = 1, if instr_op_i == 0
    R-type
    -> Multiplexer selects [15:11] as the register to write to
  - Branch = 1, if instr_op_i ∈ {4, 5}
    BEQ, BNE
- Simple_Single_CPU
  - keep_sign (KeepSign) = 1, if inst[31:26] ∈ {9, 13}
    Keep sign (Zero-extend) if op is SLTIU, ORI
  - Assign shamt ([10:6]) as the first ALU source if op is SRA
  - TakeBranch =
        BEQ -> Zero
        BNE -> !Zero
Problems Encountered and Solutions
- Errors related to timing (eg. results come 1 clock cycle later)
  Solution: Change all nonblocking assignments to blocking assignments.
- General debugging difficulties
  Debugging is a pain throughout the implementation.
  Solution: Declare an always block and use $display to see the contents in the variables during simulation (evaluation).
always @(*) begin $display("%b", inst); // $display("addr_nxt1 = %d, addr_nxt2 = %d, addr = %d, addr_nxt = %d", addr_nxt1, addr_nxt2, addr, addr_nxt); $display("%b", RegWrite); // $display("%b %b", RegRead1, reg_read1); $display("%d %d => %d ", reg_data1, reg_data2, res_alu); end

Lesson Learned (If Any)
- Debugging is surprisingly difficult with so many modules in 1 place.
  Next time it’s probably wise to test individual components first, but even that would be kind of troublesome.
- Read the samples first to make sure that I truly understand the MIPS operations.